## Slide 1: SPARK V
Robotic Research Platform

## Slide 2: SPARK V ATMEGA 16 (AVR)

## Slide 3: Fire Bird V Family Robots
FireBird V P89V51RD2
8051
FireBird V ATMEGA 2560
AVR
FireBird V LPC2148 ARM 7

## Slide 4: Fire Bird V uC Adaptor Boards
P89V51RD2
LPC2148
ATMEGA2560

## Slide 5: Basic components of the robot
Sensing
Locomotion
Control
Intelligence
Power
Communication

## Slide 6: SPARK V Technical Specification
Sensors:
  Three white line sensors
  Three IR proximity sensors
  Three directional light intensity sensors
  Two Position Encoders (optional)
  MaxBotix EZ series ultrasonic range sensors (optional)
  Servo mounted Ultrasonic Range Sensor (optional)
  Battery voltage sensing

## Slide 7: SPARK V Technical Specification
Locomotion/Actuation
  Spark V is a Two wheeled Robot with a castor wheel that supports the Robot.
  Two 60 RPM DC geared motors in differential drive configuration.
  Top Speed: 66cm/second
  L293D motor-driver controlling the direction and velocity of motor.
  Intelligence
  Microcontroller: ATMEL ATMEGA16

## Slide 8: SPARK V Technical Specification
Indicators:
  16 x 2 Alpha-numeric LCD
  LED indicators
  Buzzer
  Battery Low Indications
Communication:
  USB Communication using FT232 USB to Serial Converter
  Simplex infrared communication (From infrared remote to robot)
  ZigBee (IEEE 802.15.4) (Wireless)(Robots to Robots and Robots to PCs )(Optional)

## Slide 9: SPARK V Technical Specification
Programming:
  Using NEX Robotics Boot loader via USB port (no need of separate programmer)
Power:
  6 AA size NiMH rechargeable batteries.
  AC adaptor with exact 12V DC with 1Amp. current rating for battery charging.

## Slide 10: SPARK V Functional Block Diagram

## Slide 11: Features: ATMEGA16
  High-performance, Low-power AVR 8-bit Microcontroller
  Advanced RISC Architecture
  Up to 16 MIPS Throughput at 16 MHz
  32 Programmable I/O Lines
  16K Bytes of In-System Self-programmable Flash program memory
  512 Bytes EEPROM
  1K Byte Internal SRAM
  Four PWM Channels
  8-channel, 10-bit ADC
  Byte-oriented Two-wire Serial Interface (I2C)
  Programmable Serial USART
  Master/Slave SPI Serial Interface
  Programmable Watchdog Timer

## Slide 12: IR proximity and Directional light intensity sensors

## Slide 13: IR proximity and Directional light intensity sensors

## Slide 14: Ultrasonic range sensor

## Slide 15: Ultrasonic range sensor
  Spark V robot can be equipped with the 4 ultrasonic sensors from MaxBotix.
  Three sensors are mounted just above the 3 IR proximity sensors.
  4th Sensor can be mounted on the servo motor for taking 180 degrees scan for map making (marked as 4).
  Each sensor can sense distance range from 6 inches to 254 inches.
  Spark V robot supports EZ0 to EZ4 series of ultrasonic range sensors from MaxBotix.
  Sensor gives out analog output with 1 inch resolution. It gives output voltage of 9.8mV per inch.

## Slide 16: Ultrasonic range sensor

## Slide 17: Ultrasonic range sensor
  A small pulse trigger (more than 100uS) is given to the “RX” pin of the Sensor no. 1 from the microcontroller’s PD6 pin.
  Sensor 1 transmits ultrasonic pulse and gives out distance reading within 49mS.
  Sensor 1 triggers the Sensor 2 by transmitting a small pulse on its TX pin to the RX pin of the second sensor.

## Slide 18: White Line Sensor

## Slide 19: Positions Encoders

## Slide 20: Position Encoders

## Slide 21
Thank
You